## Slide 1: Screenprinting on the Cheap
Grades 6-12

## Slide 2: Materials Needed
a t-shirt, yucky/cheap paint brushes, an embroidery hoop, screen printing ink, a glue that isn't water-soluble (I use Mod Podge), curtain sheer material/tulle/old nylons, and a computer with a printer (or a good hand for drawing things).

## Slide 3: Find an image you like and that has good contrast. My cow needed to be "cut out," and I've only got Microsoft Paint on this computer and it worked fine.

## Slide 4: Save the image as a Monochrome Bitmap file and it will turn it black and white. If this loses all the detail, fudge around on Paint or try a different picture, haha. You could also live trace it in Illustrator if you have a newer version of the program (CS2 or higher).

## Slide 5: Print it out so the image is the size you want it on the t-shirt (and also so it's not bigger than the embroidery hoop you spent 67 cents on).

## Slide 8: After pulling the sheer curtain material/tulle/old nylons tight across the embroidery hoop (and screwing it shut real good), trace the image onto the material with a pencil with the material close to the paper, not upside down so it's far away.

## Slide 9: You should be able to see the pencil outline easily without squinting too hard. If it's too detailed, fudge some more and add in the detail.

## Slide 10: Turn the thing over and with the glue, paint all the "negative space," (all the places you don't want ink to go, the white space). Make sure the material isn't touching whatever surface you're working on otherwise you'll end up gluing the whole thing down.

## Slide 11: Some people say you can use tape to fill in the bigger area, but I think that painting the glue on all over the larger spaces is the best part.

## Slide 12: After the glue dries, center the image on the shirt face down, and I sort of stipple the ink through the material making sure it's fully saturated, but also making sure not to glob it all over the place.

## Slide 13: Carefully peel it back, wait for it to dry, and follow the "setting" directions on the ink (Speedball printing ink says to iron it on medium 3 - 5 minutes each side with a piece of cloth/paper between the iron and the ink).

## Slide 14: Voila!!!

## Slide 15: you can use your screen print over and over and over again. make sure to wash the ink of the screen when you are done or it won't work anymore.

## Slide 16: What paint? What glue?
Speedball brand Screen Printing Ink and Mod Podge glue are both what I use.
Mod Podge is a non-water-soluble glue. It cannot be washed out once it has dried.
You can tint the modge podge with a touch of paint in order for you to be able to visually see it better!!!

## Slide 17: My printed image looks pixelated and rough; help!
If you used nylons/tulle, that's probably why. I like those two fabrics if you're really on the low-cost side of DIY, but a sheer curtain material works much better as the "weave" of the fabric is much tighter, making a more detailed screen/print.

## Slide 18: Will the ink bleed through to the back layer of my shirt?
Maybe. Use caution as you would when working on a shirt any other time--put some newspaper between the front and back.

## Slide 19: Can I wash out the glue?
No, that's the whole point. The glue doesn't wash out so you can use the screen with the same image over and over again. I think it's a little too much effort to make to use just once; if that's what you want, I'd do a stencil instead.

## Slide 20: How do I do more than one color?
You and your students can separate layers in Photoshop and such and make multiple screens

## Slide 21: This

## Slide 22: To This

## Slide 23: To This!!!

## Slide 24: Another Shirt

## Slide 34: THERMOFAX SCREENPRINTING
Another alternative to traditional silk screening, Thermofax screens can be made quite easily with images that have been copied using a copier machine. (You need the ink from a copier machine to successfully make the screen.) There are new thermal imagers on the market, or you can buy a refurbished Thermofax machine from Welsh products or go on eBay and bid against tattoo artists who use them for transferring tattoo designs.

## Slide 35: Draw and make a photocopy

## Slide 36: To make the Thermofax screen from the copy, you need a carrier to securely feed the screen and the photocopy through the Thermofax machine. Put the copy on the bottom, facing up, then with the smooth side of the screen facing down on top of the copy, run them through the machine. It's the heat from the Thermofax machine that impresses the image onto the screen.

## Slide 37: Run it through the machine

## Slide 38: To find out if it worked, carefully lift one corner to see if the Thermofax machine heated the photocopy enough to make an impression on the screen. If not, run it through one more time.

## Slide 39: Now the only thing left to do is secure the screen to a frame or place duct tape all around the sides so the screen doesn't curl, and it's ready for use!

## Slide 40: Thick fabric paints work really well for this process, and I simply slap on some fabric paint along the top edge of the screen. (To make sure I've got the right side of the screen facing up, I put an arrow on the top).

## Slide 41: Here's what the screen looks like after you pull the paint down with a squeegee:

## Slide 42: Dyed fabric with white ink

## Slide 48: Wash those screens!!!
Make sure to clean your screen before the ink dries, otherwise the screen will be permanently clogged and ruined.