## Slide 1: Printing From Your Black & White Film
Enlarger to Projection Print Your Negative onto Paper
4-in-1 Printing Easel
for your RC paper
Timer for the enlarger

## Slide 2: You have:
Developed and dried your film
Cut and place the negative frames into an archival protective negative sleeve page. * Remember never cut less than three negative frames! Always place a clean sheet poster paper down onto the table laying your film down to cut it into the negative sleeve strips!
Label the negative sleeve page with:
  the date (month & year)
  your photo assignment title or what is on the roll of film
  your name

## Slide 3: You are now ready to make a contact sheet of your negative sleeve page.
What you will need as we enter the darkroom:
Your negative sleeve page.
Your photographic paper – have you written your name on the package with your sharpie?
A clean piece of glass.
Your darkroom/photo notebook to enter work notes.
Clean
Glass
sheet

## Slide 4
While the “white light” is still on:
Adjust the enlarger head up and down
  Lock and unlock the enlarger head – if it is one of the enlargers that has a locking system installed.
  Where the aperture/f-stop lens is located and how it turns to each setting
  Write down, in your notebook, the aperture ranges that particular enlarger has on it’s lens.
  For example: 2.8, 5.6, 8, 11 & 16
  Set your enlarger’s timer to 4 seconds
Enlarger Station – until told otherwise, you will continue to work at the same enlarger, so that you will have the opportunity to become accustomed to how to use that particular enlarger with some expertise.

## Slide 5
At your enlarger station:
Adjust the enlarger head up so that the light will shine on the whole sheet of photo paper. Just like we did when we did the photogram's and pinhole images
Turn the enlarger light to the lowest (dimmest aperture/light setting) remember this will be click “#1” and then turn it up twice – now you are on click #3 (on most of our enlarger’s this should be F8)
  This will be a starting point for you to determine how bright the light needs to be for your negatives.
  If your test strip is solid black then the light is too bright and you will need to lower your light to click #1 (less light).
  If your test strip is pure white with no images at all – then you need to turn your light up to a higher/brighter light click or aperture
After you leave the darkroom you can look at the
aperture/f-stop notes you made and determine what aperture or f-stop you used to print your contact sheet.
Always leave your enlarger station clean for the next student!

## Slide 6: Getting Ready to Make a Test Strip of Your Contact Sheet:
Cut a sheet of your photographic paper in half lengthwise. (You will have two 4” x 10” strips of paper.)
Take the two halves and cut them again so that you will have four test strips to use. (Your four test strips should now be 4” x 5”.)
Place all your strips back into your black bag as this will protect them from becoming “fogged” or “exposed”. Be sure to fold under the flap of the black bag so that light will not leak inside.
Raise the enlarger head so that the light will be over all the negative sleeve page and glass.
Adjust your “clicks” to #3 – as a starting point for determining the correct aperture or f-stop for your negatives.
Using a piece of mat board do graduated test strips using the timer set to four seconds. Each time you move the mat board move it to half of the negative frame below– this will help you “read” the test strip more easily.
Mark the back the photo paper with your initials with your sharpie before placing it in the chemical tray.

## Slide 7
RED
DEVELOPER
TRAY ONLY
YELLOW
OR WHITE
STOP BATH
TRAY ONLY
BLUE
FIX TRAY
ONLY
HELP KEEP THE CHEMICALS FROM CONTAMINATING
OUR PRINTS!
USE THE CORRECT TONG IN EACH CHEMICAL TRAY
IF YOU SEE SOMEONE USING THE WRONG TONG
“GENTLY” REMIND THEM TO RINSE IT AND PLACE
IT BACK IN THE CORRECT CHEMICAL TRAY!

## Slide 8: Processing Your Test Strip Use the Tongs or you lose your darkroom access!
Developer: (RED TONG) Agitate the tray continually for 1-11/2 minutes. Drip the print before moving to –
Stop Bath – (White/Yellow Tong) Agitate for 10 – 30 seconds – DRIP WELL Before moving to -
Fix – (Blue Tong) Agitate for 60 seconds – place the test strip in a tray and go out to the classroom under the “white light” to examine it. Return the test strip back to the fix for another four minutes after “reading it”
Remember to move it to the WATER RINSE
(2 minutes) and remove it and hang it to dry
You will need this test strip for your journal & grade!

## Slide 9: TIPS
If needed make adjustments to the aperture/f-stop or use the appropriate time you determined by looking at the test strip to make a contact sheet of your negative page.
Always look at the test strip by carrying it in a tray to the classroom!
Remember: black is white and white is black. So if your test strip is too dark (black) you will need LESS light; if your test strip is too white then you need MORE light; or you may need to increase your time as well.
Those of you who chose to “bracket” will probably not be able to have a perfect image of every frame on your film roll contact sheet. Select the best time for the majority of frames for your contact sheet.

## Slide 10: Printing the Contact Sheet
When you have determined the best test strip time you are ready to print the whole contact sheet.
Place your RC paper emulsion face up (the shiniest side is the emulsion side of your paper)
Place your contact negative sleeve page on top of it with the label writing so that it is readable.
Set your enlarger timer to the time your selected from your tests
and push the button!

## Slide 11: Processing Your Contact Sheet Use the Tongs or you lose your darkroom access!
Developer: (RED TONG) Agitate the tray continually for 1-11/2 minutes. Drip the print before moving to –
Stop Bath – (White/Yellow Tong) Agitate for 10 – 30 seconds – DRIP WELL Before moving to -
Fix – (Blue Tong) Agitate for 60 seconds – place the test strip in a tray and go out to the classroom under the “white light” to examine it. Return the contact sheet back to the fix for another four minutes after “checking it ”under the white light” in the classroom.
Remember to move your contact sheet to the WATER RINSE (2 minutes) and remove it and hang it to dry
You will need this contact for your grade!

## Slide 12: Judging a Contact Sheet’s Quality
A great contact sheet has readable numbers and the name brand of the film, but the “sprocket holes” are not visible.
Remember I am not grading this strictly as you are printing your first contact sheet so do the best you can and do not stress over it.
Your contact sheet should be placed in your negative/print notebook with it facing your negative sheet. The contact sheet on the left and the negative sleeve page on the right in the notebook. You may choose to punch holes directly in to the contact sheet or place it into a plastic page sleeve.
Your contact sheet is an “index” of your images for each roll of film that you shoot and a valuable tool to use for printing in the darkroom.
You are required to print a contact sheet for each roll of film that you develop.

## Slide 13
Do you have a successful roll of film for our leading lines and texture assignment?
Or do you need to go back and re-shoot the assignment using what you have learned about how to set your camera, or pay closer attention to the direction of the natural light on the object or scene?
The only way you will learn from your experience is if you take the time to look at your contact sheet and the notes you made while shooting your roll of film. If your film was not successful, then make notes about which frames worked and what your camera setting was on for those frames.
Look at the sheets posted above the light box area of the classroom. Find out what you did wrong if you do not feel that your first roll was a successful venture.
Re-shoot the roll if you do not have at least four negatives that you can print from this assignment.

## Slide 14: Everyday . . .
Be sure to always get your test strips, contact sheet or prints out of the water before you leave class each day or return to do this. I can not be responsible for making sure your prints are safe after you leave.
Squeegee the prints before placing
on the screens, or them hanging to dry.
Check the boxes for your dry prints and test strips DAILY.
Place your test strips into your journal with printing notes about that day’s darkroom session. (work ethic)
Place your dry prints into a plastic sleeve and put them into your print notebook.
Return any trays you brought into the classroom back to the darkroom before you leave for the day.
The squeegee station is by
our film developing sinks

## Slide 15: REMEMBER . . .
WORK ETHIC IS THE MOST IMPORTANT PART OF YOUR GRADE!
Students who work diligently daily and have projects that “bomb” will not fail.
Students who wait until the last minute to try to complete projects are at risk of not making the “grade”.
Photography is a class that requires failure to learn. You will continue to add the many layers of information until it all makes sense!